Service Bulletin No. 2209 / 10

Date: 22 September 2010

Application: Power Generation

Application Code: As per list given in page no. 2

Name of the part: Stamford AC Generator (Main Alternator)

Details of modification:

- Change in AC Generator, as per below details –

| Old | New |
| --- | --- |
| Description | Model | Description | Model |
| AC Generator | BC Series | AC Generator | P0 / P1 Series |

- The new range of small generators by STAMFORD, the P0 and P1, cover 7.5 to 42.5kVA at 50Hz and 9.4 to 55kVA at 60Hz in 12 core lengths.

The base machine is self-excited and designed to replace the self-excited BC range of generators. The STAMFORD P0/P1 range has been developed to meet customers need for a standardized, modular global product.

- Main Features of PO/P1 Range are :

  - Improved Rating Alignment - there are 12 P0/P1 ratings compared with 10 for BC and UC224C, increasing the probability of engine node matches

  - Enhanced Performance - improved motor starting and short circuit maintenance with the optional Excitation Boost System (EBS)

  - Reduced your Operational Cost - with reduced generating set assembly time compared with BC models

  - Easier Service and Maintenance - EBS fitted and exchangeable without disturbing the core, AVR is plug and play; diodes are accessible without removing the rotor.

Genset cut off numbers:

| Genset Model | Application Code | Cut off number |
| --- | --- | --- |
| KG 20 W | 2H.4031 | 2H.4031 / 1000001 |
| KG 30 W | 3H.4031 | 3H.4031 / 1000001 |
| KG 40 W | 4H.4031 | 4H.4031 / 1000001 |
| KG 20 WS | 2H.4081 | 2H.4081 / 1000001 |
| KG 30 WS | 3H.4081 | 3H.4081 / 1000001 |
| KG 40 WS | 4H.4081 | 4H.4081 / 1000001 |

Service Information:

Installation, Operation and Maintenance manual attached for ready reference.

This document has been created digitally and is valid without a signature.